## Slide 1: Summer 2025 Proof & Experimental Establishment (PXE), DRDO – Chandipur
Study of High-Speed Imaging Techniques and
Design & Development of a Flash Detector Circuit
Under the Guidance of:
Mr. Prem Kumar Sahani (Scientist-D)
Presented by:
Keshab Patro
B.Tech, 3rd year
Department of Electrical Engg.
National Institute of Technology, Rourkela

## Slide 2
Contents:
Overview of DRDO, PXE and Key Products
Shortcomings/ Limitations
Suggestions by the Director (PXE)
Fastest possible Flash Triggering Circuit
Constraints
Practical implementation of Flash Triggering Circuit
Experiment 2: Flash Triggering Circuit -1
Experiment 1(b): Determination of Supply Frequency Using a Fluorescent Tubelight
Experiment 1(a): Human Reaction Time –
Hands-on Experience with High-Speed camera
Single individual
Two individuals

## Slide 8
Hands-on Experience with High-Speed camera
PHOTRON FASTCAM SA5 – Key Specifications
Frame Rate:
  Up to 7,500 fps at full resolution (1,024 × 1,024 pixels)
  Up to 775,000 fps at reduced resolution (128 × 24 pixels)
Sensor Type:
  12-bit CMOS sensor (monochrome)
  Pixel size: 20 µm
Exposure Time:
  As low as 369 nanoseconds
  Typical minimum exposure time: 1 microsecond
Control Interface:
  Standalone operation using 5-inch LCD keypad
  Software control via Photron FASTCAM Viewer (PFV)
Applications:
  Ballistics (e.g., visualizing muzzle flash and projectile motion)
  Particle Image Velocimetry (PIV)
  Combustion and explosion analysis
  Aerospace

## Slide 9
Experiment- 1(a)
Average human reaction time = 0.1038 sec
= 103.8 msec
Human Reaction Time – Single individual
Objective:
To assess sensory-motor coordination, cognitive processing speed and responsiveness
Method:
Result:
                To measure the reaction time of a single individual in response to a specific stimulus
Reaction time =
Response frame – Stimulus frame
___________________________
Frame Rate
Here, Frame rate = 1000 fps
A ruler is dropped from a fixed height.
The entire action is recorded using a high-speed camera.
Reaction time is calculated by:
  Identifying the frame where the ruler is released
  Identifying the frame where it is caught
  Applying the formula:

## Slide 10
Human Reaction Time – Two individuals
Objective
To compare the reaction times of two individuals in response to a stimulus
To analyse differences in:
Cognitive processing speed
Motor coordination
Attention and decision-making ability
Method:
Reaction time =
Response frame – Stimulus frame
Frame Rate
A ruler is dropped from a fixed height.
The entire action is recorded using a high-speed camera.
___________________________
Reaction time is calculated by:
  Identifying the frame where the ruler is released
  Identifying the frame where it is caught
  Applying the formula:

## Slide 11
Average human reaction time = 0.1538 sec = 153.8 msec
Two individuals:

## Slide 12
Experiment- 1(b)
Determination of Supply Frequency Using a Fluorescent Tubelight
Procedure:
Frame rate was set to 250, 500 and 1000 fps on the high-speed camera
Camera was focused on a fixed point on the tubelight
For each frame, RGB values at that point were recorded
Graphs plotted:
R, G, B channel values vs. time
Average brightness (mean of R, G, B) vs. time
Perceived luminance vs. time
Perceived Luminance = 0.2126R + 0.7152G + 0.0722B
Supply frequency determined by analyzing the periodicity of the brightness/luminance graph or RGB values

## Slide 13
Chart: Brightness and Luminance Graphs
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Perceived Luminance | 74.113 | 103.058 | 124.2798 | 137.646 | 72.3978 | 103.054 | 124.4242 | 58.6064
Avg Brightness | 73.593 | 103.23 | 124.209 | 137.862 | 72.261 | 102.564 | 124.875 | 57.942
Chart: Pixel Values
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
R | 57 | 80 | 98 | 108 | 56 | 81 | 98 | 44
G | 78 | 108 | 130 | 144 | 76 | 108 | 130 | 62
B | 86 | 122 | 145 | 162 | 85 | 119 | 147 | 68
Chart: Brightness and Luminance Graphs
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Perceived Luminance | 141.24 | 203.61 | 210.21 | 152.46 | 96.03 | 140.91 | 203.28 | 210.54
Perceived Luminance | 143.8598 | 199.6688 | 205.1702 | 155.2942 | 97.9096 | 143.0042 | 199.3158 | 205.3828
Chart: Pixel Values
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
R | 113 | 166 | 172 | 122 | 76 | 112 | 164 | 173
G | 151 | 205 | 210 | 163 | 103 | 150 | 205 | 210
B | 164 | 246 | 255 | 177 | 112 | 165 | 247 | 255
For Frame rate = 250 fps
For Frame rate = 500 fps

## Slide 14
For Frame rate = 1000 fps
Chart: Brightness and Luminance Graphs
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Perceived Luminance | 112.53 | 120.78 | 117.15 | 101.97 | 79.2 | 58.74 | 47.85 | 54.78 | 74.58 | 94.38 | 112.2 | 120.12 | 118.14 | 102.3 | 80.19 | 59.07
Perceived Luminance | 116.3452 | 124.7796 | 121.1326 | 105.0552 | 81.9738 | 61.2454 | 49.8832 | 56.6024 | 76.6838 | 96.9056 | 116.273 | 124.7756 | 122.6352 | 105.1274 | 83.7572 | 61.3176
Chart: Pixel Values
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
R | 90 | 96 | 94 | 81 | 62 | 47 | 38 | 43 | 59 | 76 | 90 | 97 | 94 | 81 | 64 | 47
G | 123 | 132 | 128 | 111 | 87 | 65 | 53 | 60 | 81 | 102 | 123 | 132 | 130 | 111 | 89 | 65
B | 128 | 138 | 133 | 117 | 91 | 66 | 54 | 63 | 86 | 108 | 127 | 135 | 134 | 118 | 90 | 67
12-2 = 10 frames
1000 frames = 1 sec
10 frames = 0.01 sec = 10 msec = gap b/w 2 peaks
So, time period = 20 msec OR supply freq. = 50 Hz

## Slide 15
Experiment- 2
Flash Triggering Circuit – Design 1
Objective:
To design and implement a flash triggering circuit that detects the flash generated during the firing of a gun and provides a corresponding 5V output signal which will be then used to trigger a camera.

## Slide 16
Simulation Results:
The circuit performed satisfactorily both in SPICE simulation and real life testing, supporting loads as high as 0.45 A by producing a sharp pulse due to light intensity variation.
Triggering Waveform based on Intensity Variation

## Slide 17
Video of Flash Triggering Circuit – Design 1

## Slide 18
Simulation of Flash Triggering Circuit (Design 1) on Tinkercad
Note: The measured output voltage was 5V in practical testing.

## Slide 19
Shortcomings/ Limitations:
The theoretical delay of the circuit is
LDR + BC547 + UA741 + D flip flop (74LS74) + UA741 + BC547
= 100 ms + 100 ns + 20 us + 30 ns + 20 us + 100 ns
= 100 ms + 230 ns + 40 us
= 100.04023 ms
Sunlight filtering is not integrated with the LDR and temporarily implemented here using a sunglass.
Recommendations from the Director(PXE):
Minimize the circuit delay to < 1 us
(sub-microsecond level)
Target further optimization for nanosecond (ns) range if feasible

## Slide 20
Practical implementation of Flash Triggering Circuit:
Changes implemented:
Replaced the Op-Amp (UA741) and the RTL-based amplification circuit with a TTL logic-based solution using the 74LS14 (Hex Schmitt Trigger Inverter).

## Slide 21
Video of Flash Triggering Circuit

## Slide 22
Simulation on Tinkercad
Note: The measured output voltage was 5V and output current was 60-70mA in practical testing.

## Slide 23
Theoretical delay calculation:
1. Photodiode (BPW34) Response
2. BJT Amplifier (BC547) Delay
3. 74HC04 Schmitt Trigger
Propagation Delay (Vcc=5V): 15ns (datasheet max)
Two Inverters in Series: 15ns × 2 = 30ns
Rise Time (10%→90%): 100ns (datasheet value)
Junction Capacitance: 40pF @ 5V reverse bias
RC Time Constant: With 10kΩ load resistor (typical for BPW34 circuits): τ = R × C = 10kΩ × 40pF = 400ns → Actual response ≈ 2.2τ = 880ns
Transition Frequency (fₜ): 100MHz
Switching Delay: t_delay = 1/(2π × fₜ) ≈ 1.6ns (theoretical) But with parasitic board capacitance (~15pF): τ = R_load × C_parasitic = 1kΩ × 15pF = 15ns → Total stage delay ≈ 20ns

## Slide 24
4. 74HC74 D Flip-Flop
Clock-to-Q Delay: 25ns (datasheet max @ 5V)
Setup Time: 20ns (must be stable before clock edge) → Total DFF delay ≈ 45ns
5. Output Inverter Chain
Two more 74HC04 inverters: 15ns × 2 = 30ns
Cumulative Delay
Stage | Delay Contribution
BPW34 | 880ns
BC547 | 20ns
1st Inverter Pair | 30ns
74HC74 DFF | 45ns
Output Inverters | 30ns
Total | 1,005ns (≈1μs)

## Slide 25
Practical delay of this circuit measured using oscilloscope:
input
output
Input rises gradually to ~6 V after light detection.
Delay is measured from 10% level (0.6 V) to output transition.
Estimated delay ≈ 2 µs.

## Slide 26
Comparison with standard Flash Detectors available at PXE:
Experimental Setup:

## Slide 27
Comparison with standard Flash Detector-1:
Delay between the standard Flash Detector & the implemented design = 1.5-1.6 µs

## Slide 28
Comparison with standard Flash Detector-2:
Experimental Setup:

## Slide 29
Comparison with standard Flash Detector-2:
Delay between the standard Flash Detector & the implemented design = 2.2 µs
(ambient light condition)

## Slide 30
Comparison with standard Flash Detector-2:
Delay between the standard Flash Detector & the implemented design = 3 µs
(no light condition)

## Slide 31
Triggering Fastcam SA5 using the implemented design:
Note: in the previous 2 slides, the o/p voltage is 5 volts, sufficient enough to trigger the camera.

## Slide 32
Fastest possible Flash Triggering Circuit
(Theoretical Maximum Performance Implementation)
Theoretical maximum delay time = 1.05ns
(Total latency)

## Slide 33
Original | Advanced Replacement | Key Parameters | Where to Buy
BPW34 Photodiode | Hamamatsu G11193 SiPD | 0.5ns rise time, 15pF @ 12V | Digi-Key #1480-1032-ND
BC547 BJT | MACOM MA4-1315 GaAs HBT | 25GHz, 0.1ns switching | Mouser #894-MA4-1315-ITR1
74HC04 Inverter | Hittite HMC86 GaAs Inverter | 0.05ns delay, 5V operation | Arrow Electronics
74HC74 DFF | Renesas HMC7043 GaAs DFF | 0.25ns clk-to-Q, 5V tolerant | Renesas Direct
Component Replacements & Specifications:

## Slide 34
Signal Flow Architecture & Delay calculation:

## Slide 35
Performance Comparison:
Parameter | Original | Upgraded | Improvement
Latency | ~2μs | 1.05ns | 1900x
Max Trigger Rate | 10kHz | 500MHz | 50,000x
Sensitivity | 100μW | 5nW | 20,000x

## Slide 36
Implementation Constraints:
1. Cost & Availability Challenges
(With Practical Alternatives)
A. Premium Components (Theoretical Max Performance)
Component | Example Part | Price (1pc) | Lead Time
Photodiode | Hamamatsu G11193 | $420 | 18 weeks
Amplifier | MACOM MA4-1315 | $380 | 12 weeks
DFF | Renesas HMC7043 | $270 | 26 weeks
B. Practical Alternatives (90% Performance, 10% Cost)
Component | Alternative Part | Price | Performance Penalty
Photodiode | Thorlabs DET025AFC | $85 | 1ns vs 0.5ns
Amplifier | ON Semi NBSG86 | $22 | 0.15ns vs 0.1ns
DFF | TI SN74AXC1G74 | $1.20 | 3.5ns vs 0.25ns

## Slide 37
2. Severe Availability Challenges
Component | Lead Time | Stock Status (Digi-Key/Mouser)
G11193 SiPD | 18 weeks | "Factory Order"
MA4-1315 | 12 weeks | "No Stock"
HMC7043 | 26 weeks | "Military Supply Chain"
3. Procurement Challenges:
  a. Requires RF specialty distributors (Richardson RFPD, etc.)
  b. 12-16 week lead times common
  c. Not stocked on: Robu.in, Quartz Components, LCSC
  a. Rogers 4350B PCB substrate ($500/panel)
  b. Laser-drilled vias for 25GHz signals
4. Fabrication Demands:

## Slide 38
5. Side-by-Side Comparison
Parameter | Theoretical Max | Practical Alternative
Total Cost | $1,520 | $120
Latency | 1.05ns | 3ns
Max Rate | 500MHz | 200MHz
Build Time | 6-12 months | 2 weeks
Test Gear | $50k+ | $5k scope sufficient
For academic/hobbyist projects, the alternative solution provides nanosecond-scale performance without exotic components.
The 1.05ns design remains viable only for funded research or commercial applications with defense supply chain access.

## Slide 39: References:
[3] - https://www.drdo.gov.in/drdo/labs-and-establishments/proof-experimental-establishment-pxe
[4] - https://www.drdo.gov.in/drdo/labs-establishment/historical-background/proof-experimental-establishment-pxe
https://en.m.wikipedia.org/wiki/Proof_and_Experimental_Establishment
[5] - https://www.drdo.gov.in/labs-establishment/combat-vehicles-research-development-establishment-cvrde
[6] - https://www.drdo.gov.in/labs-and-establishments/armament-research-development-establishment-arde
[7] - https://www.drdo.gov.in/technology-cluster/armaments-and-combat-engineering/arde
[16] - https://pmc.ncbi.nlm.nih.gov/articles/PMC4456887/
[20] - https://www.researchgate.net/figure/R-LED-flash-detection-circuit_fig6_228506348

## Slide 40: Thank You